Technaxx®  * User Manual

Jump Starter 10000mAh TX–78

The Declaration of Conformity for this device is under the Internet link: www.technaxx.de/ (in bottom bar “Konformitätserklärung”). Before using the device the first time, read the user manual carefully. This device has a rechargeable battery. It must be fully charged before first use.

# NOTE: Charge the battery of the device every 2–3 month if it is not used!

Service phone No. for technical support: 01805 012643 (14 cent/minute from German fixed-line and 42 cent/minute from mobile networks). Free Email: support@technaxx.de

Important Hints * This device is only suitable for CARS (12V) !

( This device has 4 indicator lights. When only 2 LED are shining, or less, then do NOT use the device to start your car ! But you can use it for charging digital devices. ( When trying to start your car more than 3x without success, stop starting it. Disconnect the device to avoid damaging other parts of the car. ( Check the power of the device 1x per month and also charge it to ensure it can work in an emergency case. ( Do NOT use the device all the time for charging. Maybe then it will not have enough power for starting a car in an emergency situation. ( Device shuts down automatically when it is not loading other external devices.

Features

( 3-in-1 Power Bank: Jump Starter for the car battery, Charging (e.g. Smartphone, Tablet PC, etc.), Emergency Light ( Jump start: diesel cars up to 3L engine, gasoline/petrol cars up to 5L engine ( Integrated emergency light (3 lighting effects) ( Built-in protection against overcurrent, short circuit, overload/-charge and overvoltage ( 2 USB outputs for simultaneous charging of two devices ( 4-in-1 charging cable supports Micro USB & Mini USB & Lightning & 30-pin connector ( Ideal size to fit into the inner front glove compartment

Technical specifications

| Jump Start output | 12V output for starting a car |
| --- | --- |
| Starting current / Peak current | 300A / 400A |
| Input voltage | at home 15V/1A, in a car 12V/1A |
| Output (USB ports) | 5V/1A and 5V/2A |
| Battery Clamps | Input: DC 10.8–15V 400A, Output: DC 12V 400A |
| Battery | Lithium polymer battery with 10000mAh 3.7V/ 36.63Wh |
| Charging time | ~4 hours |
| When device is fully charged it can charge iPhone 6S ~3 times |
| When device is fully charged it can be used ~200 times |
| Operating temperature | 0°C up to +60°C |
| Storage temperature | –10°C up to +60°C |
| Weight / Dimensions | 385g / (L) 16.5 x (W) 7.3 x (H) 2.8cm |
| Package Contents | Jump Starter 10000mAh TX-78, 4-in-1 USB cable, Jump Starter cable with battery clamps, Home charger, Car charger, User Manual |

Product View

Battery clamps

12V Output for starting car

Switch button

Indicator lights = Capacity status LEDs

Working indicator light = Charging status LED

15V/1A Input

Home charger / Car charger

5V/2A USB output

5V/1A USB output

Switch button and power indication instructions

- Press the SWITCH button 1x, check the balance power and start the product.

- Press the SWITCH button for 2–3 seconds to activate the LED flasher. The 3 modes of LED lights appear in sequence (Strobe, SOS, Fast flashing warning, Off). Press short the switch button to turn off the device. This device has intelligent shutdown, means, when it is fully charged and no other device is connected to it for external charging, then it shuts down automatically to save its energy.

(3) Balance power indication ( press the SWITCH button. Then the power indicator lights are on. 4 LEDs are on, balance power is about 75%-100% ( 3 LEDs are on, balance power is about 50%-75% ( 2 LEDs are on, balance power is about 25%-50% ( 1 LED is on, balance power is about 10%-25% ( 0 LED is on, balance power is 0%.

(4) Charging power indication ( connect the charger to the device and then the power indicator lights flash.

1st LED flashes, charging power is about 0%-25% ( 2nd LED flashes, charging power is about 25%-50% ( 3rd LED flashes, charging power is about 50%-75% ( 4th LED flashes, charging power is about 75%-100% ( When 4 LEDs are on, the device is fully charged.

Power indication comparison table:

- Charging the device

Use the 15V/1A home charger or the 12V/1A car charger to charge the device, when all 4 LEDs are on (that means the device is fully charged). Disconnect the device to save the power.

- Jump Start (start-up aid) of vehicles with a 12V-on board network

  - Check and confirm that the power indicator need to light on 3 or more. Connect the battery clamps to car battery. Red battery clamp must be connected with car battery positive (+) terminal, while black clamp with negative (–) side of the car battery, making the connecting area between the clamps and battery as large as possible.

  - Insert the plug of the battery clamps into the Jump Starter.

  - Start the car with the car key.

  - Disconnect the plug within 15 seconds after the start.

  - Remove the clamps.

(6) How to charge a digital device whose input is 5V

- Choose the suitable data cable with USB connector.

- Put the USB connector into the 5V output of the Jump Starter.

- Connect the other end of the data cable to the digital device, and then press the switch button, the indicator lights are on, and charging begins.

When you use 5V output to charge digital devices, the color of LED is RED.

Trouble shooting

No response when pressing the switch button on the Jump Starter ( Cause: maybe low voltage of the Jump Starter ( Solution: plug the Jump Starter into the 15V/1A input port to charge it.

Warnings

( Do not disassemble the device by yourself (voiding the warranty). Use the original home charger to recharge the device, or it may reduce the lifetime of the device. ( Make sure the blue plug of the cable into the socket of the device tightly, otherwise it cannot jump start the vehicle, and even make the joint melt. ( Do not start up car with the car jump starter when the power is less than 75% (3 LEDs on or less) to avoid any damage. Take the product away after the car starts within 30 seconds. Otherwise may cause accidents. When finding the device expands, do not use it to start the car, to avoid safety accident. This product cannot be continuous to start the car, it may cause damage to the product. ( Each time you start the interval must be longer than 30 seconds. When staring the car continuously with 30 seconds pause, and it is not successful after 3 times, then stop starting to avoid causing damage to the device or safety accident. ( It will cause severe damage to the device when starting the car via this device continuously or use this device to start the car whose starting power is over this device, and it may cause safety accident easily. ( Do make sure the battery clamps well connected. If battery connector is rusted or dirty please clean it first, or the vehicle cannot be started. Do make sure the red clamp to the positive terminal, black clamp to the negative terminal, do not connect in the opposite way or it may damage the car. When the blue plug of the battery cable clamps is into the device, do not connect the two clamps, otherwise it will cause safety accident easily. ( Keep the device away from children. It should be only used by adults.

Indoor Storage Hints ( Make sure it is out of the kids. ( Make sure it is far from fire and the object whose surface temperature is over 60°C, to avoid severe damage or burning.   ( Make sure it is stored in no corrosive gas environment. ( Make sure it is stored in the environment between 15°C and 35°C, then the device will be originally good for 6 months.

Car Storage Hints ( Remove the product and keep it indoors when the car interior temperature is not between –10°C up to 60°C to prevent serious damage or explosion.    ( Make sure the device in the suitable position, to avoid damage caused by bumping.

Security and Disposal Hints for Batteries: Hold children off batteries. When a child swallowed a battery go to a doctors place or bring the child into a hospital promptly! Look for the right polarity (+) and (--) of batteries! Always change all batteries. Never use old and new batteries or batteries of different types together. Never short, open, deform or load up batteries! Risk of injury! Never throw batteries into fire! Risk of explosion!

Hints for Environment Protection: Packages materials are raw materials and can be recycled. Do not disposal old devices or batteries into the domestic waste. Cleaning: Protect the device from contamination and pollution (use clean drapery). Avoid using rough, coarse-grained materials or solvents/aggressive cleaner. Wipe the cleaned device accurately. Important Notice: Should battery fluid leak from a battery, wipe the battery case with a soft cloth dry. Distributor: Technaxx Deutschland GmbH & Co.KG, Kruppstr. 105, 60388 Frankfurt a.M., Germany